## Slide 1: Selective Reject ARQ

## Slide 2
Selective Reject ARQ is an error control protocol used in the Data Link Layer to ensure reliable data transmission.
Concept
  In Selective Reject ARQ, the sender retransmits only the specific frame that is lost or corrupted, not all the frames after it.
  The receiver can store the correctly received frames even if some frames are missing.

## Slide 3: Working Process
The sender sends multiple frames using a sliding window.
The receiver checks each frame for errors.
If a frame is received correctly, the receiver sends an ACK for that frame.
If a frame is lost or has an error, the receiver sends a NAK (Negative Acknowledgment) for that specific frame.
The sender retransmits only the erroneous frame.

## Slide 4: Example
Suppose the sender sends: Frame 0, 1, 2, 3, 4
Frame 0 → Correct (ACK0)
Frame 1 → Correct (ACK1)
Frame 2 → Error
Frame 3 → Correct (stored)
Frame 4 → Correct (stored)
Receiver sends NAK2, and the sender retransmits only Frame 2.

## Slide 5
Advantages
  More efficient than Go-Back-N ARQ
  Only the incorrect frame is retransmitted
  Better bandwidth utilization
Disadvantages
  More complex to implement
  Receiver must have larger buffer to store out-of-order frames

## Slide 6
Selective Reject ARQ retransmits only the frames that contain errors, making it more efficient than Go-Back-N ARQ.

## Slide 7: Comparison: Go-Back-N ARQ vs Selective Reject ARQ
Feature | Go-Back-N ARQ | Selective Reject ARQ (Selective Repeat)
Retransmission | Retransmits the erroneous frame and all subsequent frames | Retransmits only the erroneous frame
Receiver Behavior | Discards all frames received after the error frame | Stores correct frames even if some frames are missing
Efficiency | Less efficient because many frames may be retransmitted | More efficient since only the wrong frame is sent again
Buffer Requirement | Requires small buffer at the receiver | Requires larger buffer to store out-of-order frames
Complexity | Simpler to implement | More complex
Bandwidth Usage | More bandwidth waste due to multiple retransmissions | Better bandwidth utilization
Application Layer | Used in the Data Link Layer for error control | Also used in the Data Link Layer