## Slide 1: Go-Back-N ARQ

## Slide 2
Go-Back-N ARQ (Automatic Repeat reQuest) is an error control protocol used in the Data Link Layer to detect and recover from errors during data transmission.
Concept
  In Go-Back-N ARQ, the sender can transmit multiple frames at a time using a sliding window. If a frame is lost or contains an error, the sender must go back and retransmit that frame and all subsequent frames.

## Slide 3: Working Process
The sender sends several frames continuously without waiting for acknowledgment for each one.
The receiver sends ACK (Acknowledgment) for correctly received frames.
If a frame is lost or received with an error, the receiver discards that frame and all following frames.
When the sender’s timer expires (timeout), it retransmits the erroneous frame and all frames sent after it.

## Slide 4: Example
Suppose the sender sends the following frames: Frame 0, 1, 2, 3, 4
Frame 0 → Correct (ACK0)
Frame 1 → Correct (ACK1)
Frame 2 → Error
Frame 3, 4 → Discarded by the receiver
The sender then retransmits: Frame 2, 3, 4

## Slide 5
Advantages
  Higher efficiency than Stop-and-Wait protocol
  Allows multiple frames to be sent before receiving ACK
Disadvantages
  If one frame has an error, many frames may need to be retransmitted
  This may waste bandwidth